#22   Visible Spectrum of Chlorophyll from Spinach

_______________________________________________________________________

Purpose: Chlorophyll is extracted from spinach.  From a spectrum of the solution produced, the ratio of chlorophyll a and b present is estimated.

Introduction:  A spectrum is a recording of the wavelengths absorbed by a sample.  Colored compounds, such as the green chlorophyll in this experiment absorb in the visible.

The transmittance, %T, is the ratio of the intensity of the incident light ( I0) and the intensity of the emerging light  ( I ), or %T = I / I0.  Absorbance, A, is the logarithm of 100 divided

by %T :

If %T = 50, then, A = log 100/50 = log 2 = 0.30

Find 50% T on the meter scale and notice that it corresponds to 0.30 on the Absorbance scale.  The  % T scale is linear and increases from left to right. The A scale is logarithmic and increases from right to left.  It is more accurate to read % transmittance rather than absorbance, so record %T values and convert to A.

Extraction

In solid extraction, a liquid is used to remove one or more substances from a mixture  of solids, often those that occur in nature.  In this experiment the solid mixture is spinach, the liquid solvent is ethanol, CH3CH2OH,  and the substance to be isolated is chlorophyll.

Chlorophylls

Plants synthesize carbohydrates (sugars and starches) from CO2 and H2O through a complex set of reactions called photosynthesis.  The first step is the absorption of sunlight by chlorophyll molecules in plants. There are two chlorophylls with closely related structures. The ‘a’ compound has a methyl group, CH3, where the ‘b’ form has an oxygen containing group, CHO.  These are in bold in the formulas below.

The visible absorption spectra of the two chlorophylls are different.  The plot on the right is a spectrum  of spinach extract. The peak at 430 nm is due to chlorophyll a.  The shoulder at 460 nm is from chlorophyll b.

Note that both chlorophylls have a second weaker absorption  between 600 and 680 nm.

##### Apparatus

The Spectronic-20 will be used to take a spectrum of the chlorophyll solution. To use the instrument refer to the operating instructions attached.

Procedure

Part A:  Extracting Chlorophyll from Spinach

1. Shred a medium-sized leaf of spinach and mix with 10 mL of ethanol in a 50 mL beaker.  After approximately 5 minutes, the solution should have a green tint.

Note:  If the solution looks yellow, the extraction is not finished.

2. Filter the mixture of leaves and ethanol into another 50-mL beaker, using a funnel with a fluted filter.  Discard the spinach.

###### Part B:  Spectrum of Chlorophylls

1. Fill one cuvette with ethanol (the blank) and another with the solution of chlorophylls (the sample). First, check the absorbance at 440 nm. The reading there, where both chlorophylls absorb to some extent,  should be somewhere between 0.3 and 0.8. If the solution is too concentrated, pour the sample into a graduated cylinder and add an equal amount of alcohol to dilute the solution by half. Check the absorbance at 440 again.  Dilute further if needed. Record the dilution needed.

2. Set the wavelength dial to 400 nm and measure the % transmittance of your sample.  Continue to measure the % T every 10 nm between 400 nm and 700 nm, remembering to adjust the instrument to full scale at each new wavelength.  You can take readings every 5 nm between 420 and 480 to make it easier to observe the absorption due to both chlorophylls.

3.  Convert % T  to A.  Plot absorbance vs. wavelength by drawing a smooth line through the points (do not “connect the dots”).

4. Compare the spectrum with the one above to find evidence for presence of both chlorophyll a and b.   Estimate the relative amounts of a and b in your sample.

Data and Results (Chlorophyll)

Name(s)__________________________________________________________________

Part B:  Spectrum of Chlorophylls

Dilution(if required):  Vol. Leaf Extract ______mL   Vol. Alcohol added:  ______ mL

|  nm | %T | A |  nm | %T | A |
| --- | --- | --- | --- | --- | --- |
| 400 |  |  | 530 |  |  |
| 410 |  |  | 540 |  |  |
| 420 |  |  | 550 |  |  |
| 425 |  |  | 560 |  |  |
| 430 |  |  | 570 |  |  |
| 435 |  |  | 580 |  |  |
| 440 |  | . | 590 |  |  |
| 445 |  |  | 600 |  |  |
| 450 |  |  | 610 |  |  |
| 455 |  |  | 620 |  |  |
| 460 |  |  | 630 |  |  |
| 465 |  |  | 640 |  |  |
| 470 |  |  | 650 |  |  |
| 475 |  |  | 660 |  |  |
| 480 |  |  | 670 |  |  |
| 490 |  |  | 680 |  |  |
| 500 |  |  | 690 |  |  |
| 510 |  |  | 700 |  |  |
| 520 |  |  |  |  |  |

Estimated amount of chlorophyll a/chlorophyll b  ______________

Questions:

1. Why is it necessary to shred the spinach before extraction?

2. How do plants benefit from the presence of both chlorophyll a and b?

__________________________________________________________________________

Instructor’s Guide

(#22 Chlorophyll)

Data and Results (Chlorophyll)

Part B:  Spectrum of Chlorophylls

Dilution(if required):  Vol. Leaf Extract ______mL   Vol. Alcohol added:  ______ mL

|  nm | %T | A |  nm | %T | A |
| --- | --- | --- | --- | --- | --- |
| 400 |  | 0.252 | 530 |  | 0. 0223 |
| 410 |  | 0.284 | 540 |  | 0. 0223 |
| 420 |  | 0.323 | 550 |  | 0. 0223 |
| 425 |  | 0.328 | 560 |  | 0.0269 |
| 430 |  | 0.342 | 570 |  | 0.0315 |
| 435 |  | 0.347 | 580 |  | 0.0339 |
| 440 |  | 0. 347 | 590 |  | 0.041 |
| 445 |  | 0.328 | 600 |  | 0.0458 |
| 450 |  | 0.305 | 610 |  | 0.0506 |
| 455 |  | 0.276 | 620 |  | 0.0555 |
| 460 |  | 0.260 | 630 |  | 0. 0555 |
| 465 |  | 0.237 | 640 |  | 0.0655 |
| 470 |  | 0.229 | 650 |  | 0.102 |
| 475 |  | 0.215 | 660 |  | 0.146 |
| 480 |  | 0.184 | 670 |  | 0.143 |
| 490 |  | 0.114 | 680 |  | 0.0861 |
| 500 |  | 0.0555 | 690 |  | 0.0362 |
| 510 |  | 0.0292 | 700 |  | 0.0088 |
| 520 |  | 0.0223 |  |  |  |

Questions:

1. Why is it necessary to shred the spinach before extraction?   Ans: More surface area comes into contact with the ethanol,  speeding up the process of extraction.

2. How do plants benefit from the presence of both chlorophyll a and b?  Ans: Since the two chlorophylls absorb strongly at different wavelengths, 430nm and 460nm, plants can  capture more sunlight.

__________________________________________________________________________

Instructor’s Guide (cont’d)

(Chlorophyll)

Equipment and Materials:

| Items | Am’t/gp | Comment |
| --- | --- | --- |
| Spinach | 1 | Fresh spinach is best |
| Ethanol | 10 mL |  |
| Funnel | 1 |  |
| Fluted filter paper | 1 |  |
| 50 mL beaker | 2 | Extraction and filtering steps |
| Spectronic-20 | 1 |  |
| Cuvettes/tubes | 2 | 1 for sample and 1 for blank |
| 10-mL graduate | 1 | For dilution |
| Safety glasses | 1 per student |  |
| Rubber gloves | 1 box per class |  |

###### Ideas/Information

Spinach is used in this experiment because its pigments are primarily chlorophyll.  Red, yellow and orange pigments called carotenoids are present in other leaves.  These absorb strongly in the blue and violet, producing a broad band in that region, making it difficult to see the chlorophyll a and b peaks at 430nm and 460nm.  The colorful carotenoids cannot be seen until autumn when the chlorophyll begins to break down.

In most plants the amount of chlorophyll a is about 3 times that of chlorophyll b.

Variations

1. Try other leaves to notice the additional absorbance due to carotenoids.

2. In the autumn, compare green leaves with the same kind of leaves that have turned color.

3. Try other very dark green leaves.