## #7 Visible Spectrum of Food Colors

________________________________________________________________________

Purpose:

Compare the visible spectra of different brands of food dyes.

###### Introduction:

A spectrum is a recording of the wavelengths absorbed by a sample. Colored compounds, such as the food colors used in this experiment absorb in the visible.

Light Source      prism or        food dyes       detector

Grating

The transmittance, %T, is the ratio of the intensity of the incident light ( Iº) and the intensity of the emerging light  ( I ), or %T = I / I˚

Absorbance, A, is the logarithm of 100 divided by %T:

A = log (100/  %T )

If %T = 50, then A = log 100/50 = log 2 = 0.30

Find 50% T on the meter scale and notice that it corresponds to 0.30 on the Absorbance scale.  The  % transmittance scale is linear and increases from left to right. The Absorbance scale is Logarithmetic and increases from right to left.  It is more accurate to read % transmittance rather than absorbance, so record the %T values and convert them to A.

##### Apparatus

You will be taking a spectrum of

food dyes using a Spectronic-20.

To use this instrument refer to the

operating instructions attached.

##### Procedure

Choose one color and take samples of different brands for that color.

Taking the Spectrum of  Food Dye

1.  The samples you are provided have been prepared by adding one drop of food coloring to a volumetric flask then diluting with water to 100 mL.  Pour each of the samples into its own cuvette to a level of approximately 2 cm.  Be careful to identify which brand is which and record the brand names in the data table.  Also, prepare a blank cuvette using distilled water.  (The blank is used to adjust for a full scale indication at each wavelength.) Find the %T measurement at 400 nm for each sample.

2.  Measure the % transmittance every 10 nm between 400 nm and 700 nm (remembering to adjust the transmittance control for a full scale indication using a blank at each new wavelength).  Record %T.

Note: At 600 nm the filter selection lever must be switched.

After determining the approximate wavelengths of the maximum absorbance (minimum transmittance) of the solution you may want to “redo” the region around the peak wavelengths proceeding with smaller steps in order to make the peak wavelength determinations more accurate. Some dyes, such as green, have more than one peak.

When you are through taking the spectrum, keep the solutions.  When you find a difference among spectra of different brands, you can also try to see the difference by eye.

3.  Convert % transmittance to absorbance. Make a plot of absorbance vs. wavelength for each of the solutions, by drawing a smooth line through the points.   This is the visible spectrum of the stock solutions of food dye.

4.  Record the wavelength(s) at which the maximum absorbance is observed and the peak height(s).  Include the major peaks.   Compare for each brand.   The larger the peak height the greater the concentration.  Estimate the concentrations of different brands of the same color.

Note:  The drops are similar in size. One drop of McCormick’s weighs about 3 g and 1 drop of a generic brand (such as Tone’s) weighs closer to 4 g.

Data and Results (Spectra of Food Colors)

Name(s) ______________________________________________________________

Color_______________

| Brand: McCormick’s | Brand: |
| --- | --- |
| nm | %T | A | nm | %T | A |
| 400 |  |  | 400 |  |  |
| 410 |  |  | 410 |  |  |
| 420 |  |  | 420 |  |  |
| 430 |  |  | 430 |  |  |
| 440 |  |  | 440 |  |  |
| 450 |  |  | 450 |  |  |
| 460 |  |  | 460 |  |  |
| 470 |  |  | 470 |  |  |
| 480 |  |  | 480 |  |  |
| 490 |  |  | 490 |  |  |
| 500 |  |  | 500 |  |  |
| 510 |  |  | 510 |  |  |
| 520 |  |  | 520 |  |  |
| 530 |  |  | 530 |  |  |
| 540 |  |  | 540 |  |  |
| 550 |  |  | 550 |  |  |
| 560 |  |  | 560 |  |  |
| 570 |  |  | 570 |  |  |
| 580 |  |  | 580 |  |  |
| 590 |  |  | 590 |  |  |

switch filter

| 600 |  |  | 600 |  |  |
| --- | --- | --- | --- | --- | --- |
| 610 |  |  | 610 |  |  |
| 620 |  |  | 620 |  |  |
| 630 |  |  | 630 |  |  |
| 640 |  |  | 640 |  |  |
| 650 |  |  | 650 |  |  |
| 660 |  |  | 660 |  |  |
| 670 |  |  | 670 |  |  |
| 680 |  |  | 680 |  |  |
| 690 |  |  | 690 |  |  |
| 700 |  |  | 700 |  |  |

Data and Results 2 (Spectra of Food Colors)

| Brand | Maximum Wavelength(s) | A (or A’s) at Maximum |
| --- | --- | --- |
| McCormick’s |  |  |

###### Question

1.  Compare concentrations of the two brands of the same color.  (See Step 4 in the Procedure).

2.  Attach the spectra.  Try to put both brands on the same graph.  Comment on any differences. (Some colors may show almost no difference.)

___________________________________________________________________________

Instructor’s Guide

(#7 Spectra of Food Colors)

Color green

| Brand: McCormick’s | Brand: Tone’s |
| --- | --- |
|  nm | %T | A |  nm | %T | A |
| 400 | 42.5 | 0.37 | 400 | 40 | 0.40 |
| 410 | 40.5 | 0.39 | 410 | 37 | 0.43 |
| 420 | 41 | 0.39 | 420 | 38 | 0.42 |
| 430 | 42 | 0.38 | 430 | 41.5 | 0.38 |
| 440 | 45 | 0.35 | 440 | 45 | 0.35 |
| 450 | 48 | 0.32 | 450 | 48 | 0.32 |
| 460 | 54 | 0.27 | 460 | 55 | 0.26 |
| 470 | 63 | 0.20 | 470 | 63 | 0.20 |
| 480 | 72.5 | 0.14 | 480 | 72.5 | 0.14 |
| 490 | 83 | 0.08 | 490 | 84.5 | 0.07 |
| 500 | 91 | 0.04 | 500 | 89 | 0.05 |
| 510 | 95 | 0.02 | 510 | 90.5 | 0.04 |
| 520 | 93 | 0.03 | 520 | 90.5 | 0.04 |
| 530 | 92 | 0.04 | 530 | 88 | 0.06 |
| 540 | 89 | 0.05 | 540 | 82.5 | 0.08 |
| 550 | 85 | 0.07 | 550 | 76.5 | 0.12 |
| 560 | 79 | 0.10 | 560 | 68.5 | 0.16 |
| 570 | 72 | 0.14 | 570 | 61 | 0.21 |
| 580 | 65 | 0.19 | 580 | 51.5 | 0.29 |
| 590 | 58 | 0.24 | 590 | 42 | 0.38 |

switch filter

| 600 | 49.5 | 0.31 | 600 | 33.5 | 0.47 |
| --- | --- | --- | --- | --- | --- |
| 610 | 37 | 0.43 | 610 | 23 | 0.64 |
| 620 | 29 | 0.54 | 620 | 16 | 0.80 |
| 630 | 25 | 0.60 | 630 | 13.5 | 0.87 |
| 640 | 31 | 0.51 | 640 | 18 | 0. 74 |
| 650 | 48 | 0.32 | 650 | 34 | 0.47 |
| 660 | 67 | 0.17 | 660 | 54 | 0.27 |
| 670 |  |  | 670 |  |  |
| 680 |  |  | 680 |  |  |
| 690 |  |  | 690 |  |  |
| 700 |  |  | 700 |  |  |

Instructor’s  Guide

(Spectra of Food Color, cont’d)

Color green

| Brand | Maximum Wavelength(s) | A (or A’s) at Maximum |
| --- | --- | --- |
| McCormick’s | 630, 410 | 0.60, 0.39 |
| Tone’s | 630, 410 | 0.87, 0.43 |

###### Question

1.  Compare concentrations of the two brands of the same color.  (See Step 4 in the Procedure).

2.  Attach the spectra.  Try to put both brands on the same graph.  Comment on any differences. (Some colors may show almost no difference.)

___________________________________________________________________________

1.  Green:  Absorbance at 630 and 410 for Tone’s is greater.  Since the Tone’s drop was a little larger, the concentrations are about the same.  However, Tone’s is cheaper.

2.  The 630 peak for Tone’s is larger and the 410 peak is a little smaller.

Instructor’s Guide

(Spectra of Food Color, cont’d)

Time:    1 1/2

Equipment and Materials:  Per group:

| Items | Number | Comment |
| --- | --- | --- |
| Cuvette stand | 1 |  |
| Wash bottles | 1 | distilled water |
| Spectronic-20 | 1 |  |
| Food dye samples | 2 | McCormick’s and Tone |
| Kim wipes | 1 |  |
| Cuvettes | 3 |  |
| Funnel | 1 |  |

###### Ideas/ Information

1.  Different brands are very similar in concentration and color as can be seen from their spectra.  However, the generic brands are cheaper.