#9 Beer’s Law, Neodymium Chloride

_______________________________________________________________________

Purpose: Using Beer’s Law you will find the concentration of neodymium chloride from the amount of light absorbed by its solution.

Background:

A spectrum is a recording of the wavelengths absorbed by a sample.  Colored compounds, such as the pale violet neodymium chloride used in this experiment absorb in the visible.

Light Source     prism               NdCl3         detector

or grating           solution

The transmittance, %T,  is the ratio of the intensity of the incident light  ( Iº) and the intensity of the emerging light  ( I ), or %T = I / I˚.   Absorbance, A,  is the logarithm of 100 divided by %T :

A =  log (100/ %T)

Notice that 50% T on the meter scale corresponds to log 2 or 0.30 on the Absorbance scale. It is easier to read % T rather than A, so record the %T values and convert them to A

Beer’s Law

According to Beer’s Law, the absorbance (A) of a solution is proportional both to the molarity of the solute and to the path length (b) of solution:

A =  (  x  b  x  molarity

The constant (  is the extinction coefficient, which depends on the wavelength of light, the solvent and the solute. The path length is the diameter of the tube used to hold the sample (The diameter of the supplied cuvettes is 1 cm).  In general, Beer’s Law works well for relatively dilute solutions.  For neodymium chloride, deviations are observed at concentrations greater than 0.125 M.

# The Lanthanides

The lanthanides (elements 58 -71) are also known as the “rare earths”.  Compounds of the lanthanides have interesting visible spectra which consist of several sharp peaks.  In this experiment you will study the spectrum of neodymium chloride solutions (Nd is element 60).   Note that neodymium chloride is hydrated, NdCl3. 6H2O and its molar mass is 358.6 g/mol.

##### Apparatus

You will be taking a spectrum of neodymium chloride solution using a Spectronic-20. To use the instrument refer to the operating instructions attached.

Safety and Waste Disposal

Wear safety glasses and gloves.  Waste bottles are available for all used NdCl3 solutions.

Procedure

Part A:  Taking the Spectrum of the Stock Solution of Neodymium Chloride

1.  Fill one cuvette with water (the blank) and another with the NdCl3 solution.  Record sample concentration from the label.  It will be about 0.125 M.

2. Set the wavelength dial to 400 nm and measure the % transmittance of your sample as described before.  Continue to measure the % T every 5 nm between 400 nm and 650 nm, remembering to insert the blank and adjust for 100 % transmittance at each new wavelength. When you finish taking the spectrum, pour the solution into the bottle marked “Used NdCl3 solution”.

3.  Convert % transmittance to absorbance. Make a plot of absorbance (y axis) vs. wavelength (x axis) by drawing a smooth line through the points (drawn to reflect experimental error).   This is the visible spectrum of the stock solution of neodymium chloride. Submit the plot with your lab report. Record the wavelength at which the maximum absorbance is observed.

Part B:  Measuring Absorbance of Diluted Solutions of Neodymium Chloride

To verify Beer’s Law you will measure absorbance at the maximum wavelength of the spectrum found in Part A.  Four solutions have been prepared:  0.100 M, 0.0750 M,

0.0500 M, and 0.0250 M.

1.  Measure the % T of each solution at the peak wavelength observed in Part A. Record the concentration.  You can do these in any order.

When you finish taking each spectrum, pour the used solution into the bottle marked “Used  NdCl3 solution”.

2.  Convert % transmittance to absorbance. Plot the absorbance (x axis) for each solution vs. the concentration (y axis).  Be sure to make the points reflect the experimental error. The plot should produce a straight line. Submit the plot with your data and results.

Note: Remember that the point 0,0 is also a data point.

3. To find (,  the extinction coefficient,  use the equation m=(y2-y1)/(x2-x1), where y1 and y2 are two different concentrations and x1 and x2 are the corresponding absorbance points.

Part C:  Determining the Concentration of an Unknown Neodymium Chloride Solution

1.   Record the code number/letter of your unknown.  Measure the % transmittance of the sample at the peak wavelength used for the known samples, convert to A and use the extinction coefficient calculated in Part B to find the concentration of your unknown using the equation:  molarity = A/((x b)

Data and Results (Beer’s Law NdCl3)

Name(s) _________________________________________________Date __________

Part A:  Taking the Spectrum of the Stock Solution of Neodymium Chloride

Concentration of NdCl3 stock solution (see label) ____________ M

| nm | %T | A |  nm | %T | A |
| --- | --- | --- | --- | --- | --- |
| 400 |  |  | 530 |  |  |
| 405 |  |  | 535 |  |  |
| 410 |  |  | 540 |  |  |
| 415 |  |  | 545 |  |  |
| 420 |  |  | 550 |  |  |
| 425 |  |  | 555 |  |  |
| 430 |  |  | 560 |  |  |
| 435 |  |  | 565 |  |  |
| 440 |  |  | 570 |  |  |
| 445 |  |  | 575 |  |  |
| 450 |  |  | 580 |  |  |
| 455 |  |  | 585 |  |  |
| 460 |  |  | 590 |  |  |
| 465 |  |  | 600 |  |  |
| 470 |  |  | 605 |  |  |
| 475 |  |  | 610 |  |  |
| 480 |  |  | 615 |  |  |
| 485 |  |  | 620 |  |  |
| 490 |  |  | 625 |  |  |
| 500 |  |  | 630 |  |  |
| 505 |  |  | 635 |  |  |
| 510 |  |  | 640 |  |  |
| 515 |  |  | 645 |  |  |
| 520 |  |  | 650 |  |  |
| 525 |  |  | 655 |  |  |

Wavelength where absorbance is maximum, max:  _________ nm

Absorbance at max:   _________

Data and Results 2 (Beer’s Law NdCl3)

Part B:  Measuring Absorbance of Diluted Solutions of Neodymium Chloride

| Molarity | %Transmittance | Absorbance |
| --- | --- | --- |
| 0.125 |  |  |
| 0.100 |  |  |
| 0.0750 |  |  |
| 0.0500 |  |  |
| 0.0250 |  |  |

Path length: ________cm

Beer’s Law constant, ( : _________M-1cm-1

(Attach absorbance vs. concentration plot)

Part C:  Determining the Concentration of an Unknown

Code number/letter of the Unknown:  __________

Absorbance at max:  ____________

Concentration of the Unknown: ____________ M

Questions:

1.  Would you be able to use your data to find the concentration of a 1.00 M solution of        neodymium chloride?  Why or why not?

2.  Describe two different methods that could be used to prepare 100 mL of a 50% solution     starting from a stock (100%) solution of 0.100 M NdCl3.6H2O (358.6 g/mol).

__________________________________________________________________________

Instructor’s Guide

(Beer’s Law NdCl3)

Part A:  Taking the Spectrum of the Stock Solution of Neodymium Chloride

Concentration of NdCl3 stock solution (see label)  0.125    M

|  (nm) | %T | A |  (nm) | %T | A |
| --- | --- | --- | --- | --- | --- |
| 400 | 99.5 | 0.00 | 530 | 75.6 | 0.12 |
| 405 | 99.5 | 0.00 | 535 | 84.4 | 0.07 |
| 410 | 100 | 0.00 | 540 | 92 | 0.04 |
| 415 | 99 | 0.00 | 545 | 95.8 | 0.02 |
| 420 | 97.8 | 0.01 | 550 | 97 | 0.01 |
| 425 | 96.5 | 0.02 | 555 | 93.4 | 0.03 |
| 430 | 96.5 | 0.02 | 560 | 87 | 0.06 |
| 435 | 97 | 0.01 | 565 | 79 | 0.10 |
| 440 | 97.2 | 0.01 | 570 | 63 | 0.20 |
| 445 | 96.2 | 0.02 | 575 | 49.2 | 0.31 |
| 450 | 97 | 0.01 | 580 | 46 | 0.34 |
| 455 | 94.2 | 0.03 | 585 | 51.2 | 0.29 |
| 460 | 92 | 0.04 | 590 | 63.5 | 0.20 |
| 465 | 88 | 0.06 | 600 | 88.5 | 0.05 |
| 470 | 86.6 | 0.06 | 605 | 95 | 0.02 |
| 475 | 85.5 | 0.07 | 610 | 97 | 0.01 |
| 480 | 88.4 | 0.05 | 615 | 97.5 | 0.01 |
| 485 | 89.5 | 0.05 | 620 | 97.5 | 0.01 |
| 490 | 90 | 0.05 | 625 | 97 | 0.01 |
| 500 | 82.5 | 0.08 | 630 | 95.8 | 0.02 |
| 505 | 75.2 | 0.12 | 635 | 96 | 0.02 |
| 510 | 67.5 | 0.17 | 640 | 97 | 0.01 |
| 515 | 60 | 0.22 | 645 | 97.6 | 0.01 |
| 520 | 60 | 0.22 | 650 | 97 | 0.01 |
| 525 | 64.7 | 0.19 | 655 | 97 | 0.01 |

Wavelength where absorbance is maximum, max:  ___580______ nm

Absorbance at max:   ___0.34______

(Spectrum is on the page with Ideas/ Information)

Part B:  Measuring Absorbance of Diluted Solutions of Neodymium Chloride

| Molarity | %Transmittance | Absorbance |
| --- | --- | --- |
| 0.125 | 46 | 0.34 |
| 0.100 | 61 | 0.22 |
| 0.0750 | 69 | 0.16 |
| 0.0500 | 78 | 0.11 |
| 0.0250 | 88 | 0.05 |

Path length:     1.00         cm               Beer’s Law constant, ( :     0.46     M-1cm-1

from: Excel and equation (y = 0.463 x)  of trendline;  retaining 2 significant figures.

Part C:  Determining the Concentration of an Unknown

Code number/letter of the Unknown:  ___ N-1______

Concentration of the Unknown: ____0.0650____ M

Code number/letter of the Unknown:  ____N-2______

Concentration of the Unknown: ____0.0976____ M

Code number/letter of the Unknown:  ___N-3____

Concentration of the Unknown: ____0.0325___ M

Answers to Questions:

1.  Would you be able to use your data to find the concentration of a 1.00 M solution of

neodymium chloride?  Why or why not?

No, because Beer’s Law does not hold for such a high concentration. (See Background)

2.  Describe two different ways that could be used to prepare 100 mL of a 0.0500 M solution

starting from a stock (100%) solution of 0.100 M NdCl3.6H2O (358.6 g/mol).

a) Mix 50.0 mL stock solution with 50.0 mL distilled water using a burette or pipet to measure the volumes.

b)  Find the mass in grams needed and use a volumetric flask:

0.050 mol/L  x 0.10 L  x 358.6 g/mol   =   1.79 g

Place 1.79 g NdCl3.6H2O in a 100 mL volumetric flask and dilute to the mark.

Time:    1 1/2 hours

Equipment and Materials (per group)

| Items | amount/no. | comment |
| --- | --- | --- |
| Wash bottles, distilled water | 1 | distilled water; to fill blank cuvette |
| Spectronic-20 | 1 |  |
| Stock 0.125M NdCl3 | 5 mL | 500 mL for whole class |
| 4 other samples: 0.100, 0.0750, 0.0500, 0.0250 M | 5 mL ea | 500 mL for whole class |
| Cuvettes or 1-cm tubes | 6 | 1 for blank; 5 for samples |
| Cuvette stand | 1 |  |
| Waste sample bottle | 1/class |  |
| Unknown solutions | 5 mL | N-1, N-2, N-3 (500 mL each for whole class) |
| Plastic funnel | 1 |  |
| Safety glasses | 1 pair per student |  |
| Rubber gloves | 1 pair per student |  |

Ideas/ Information

# 1. The Lanthanides     The lanthanide ions have interesting visible spectra that arise from electronic transitions among f orbitals.  The 4f orbitals involved are effectively shielded from their chemical environments by outer 5s and 5p electrons.  As a result the spectra arising from f-f electronic transitions are extremely sharp and are unaffected by the anions. The spectra of NdCl3 and Nd(NO3)3 are virtually identical.

2.  Solutions could be prepared by diluting the stock solution , but it is more convenient  to prepare given volumes of each solution separately. Molar mass NdCl3. 6H2O is 358.6 g/mol

| Molarity mol/L | g for 1 L solution | g for 500 mL solution | g for 100 mL solution |
| --- | --- | --- | --- |
| 0.125 | 44.8 | 22.4 | 4.48 |
| 0.100 | 35.9 | 17.95 | 3.59 |
| 0.0750 | 26.9 | 13.45 | 2.69 |
| 0.0500 | 17.9 | 8.95 | 1.79 |
| 0.0250 | 8.96 | 4.48 | 0.896 |
| N-2 0.0976 | 35.0 | 17.5 | 3.50 |
| N-1 0.0650 | 23.3 | 11.65 | 2.33 |
| N-3 0.0325 | 11.7 | 5.85 | 1.17 |